## Slide 1: Secure Scripting--Python
Advanced Control

## Slide 2: Learning Objectives
Upon completion of this unit:
2.1 Students will be able to merge two or more scripts into one that performs the same functions.
2.2 Students will be able to use loop structures in the script. 2.3 Students will be able to use variables in the script.
2.4 Students will be able to do simple arithmetic in the script.
2.5 Students will be able to use Boolean operators to test conditions in the script.
2.6 Students will be able to read, write, execute files
2.7 Students will be able to define and call functions
2.8 Students will be able to process options given to the script.
2.9 Students will be able to perform basic error checking in the script.

## Slide 3: The Problem
When an attacker compromises a system, she often changes file attributes or contents.
Our job: Write a script that checks for changes to files in a directory.
So, which aspects of the files (i.e., attributes, content) do we care about?
Notes: This sets up the problem we’ll use to demonstrate various control and data structures of scripts.
This is a common security need, and various commercial tools such as tripwire and tiger do this. They are not scripts, but they work very much like what is here.
You might mention that, in practice, one would put the files we will create in places other than where this exercise puts them. Normally the files would go in a protected area, but here I opt for simplicity.

## Slide 4: File Attributes
Protection mode
Number of links
Owner
Group
Size in bytes
Date and time of last modification
Name
Contents
Notes: There are other attributes, such as i-node number, device number, time of last access, and time of last change to i-node (as opposed to time of last change to the file). Getting these requires some fancy commands and formatting (basically, call stat(1) and collapse the output into a line), and it seemed easier not to do this in this unit.
All of these can be obtained from the widely used “ls” command.

## Slide 5: Step 1. Understand the Problem
Record the file attributes and name in a file.
Later, generate a new record of the file attributes and name.
Compare the new ones with the ones in the file.
Report the names of the files that have changed.
Notes: In practice, we would take special care of the file holding the attributes and names (keep them on write-once media, etc.).

## Slide 6: Step 2. Understand the Format of the Data
All data generated internally, by programs
  (Probably) cannot control the format these programs use
  Can manipulate their output to the form we want
So let’s look at the programs …
Notes: The lesson to be drawn here is that sometimes data needs to be extracted from systems (for example, current network bandwidth, free space on a file system, and so forth). In that case, we can either write our own programs to extract the information and put it in a form we can use, or we can see if programs exist to extract the information and then reformat it. When scripting, it’s usually much easier to do the latter, and here we can do it. So we do.

## Slide 7: Linux Programs to Consider
ls –l
  Lists the first seven attributes
shasum
  Computes a hash of the file contents
diff
  Compares two text files and lists the lines that have changed
Notes: Students might have found these on their own, as they looked around in Unit 1. The focus of this unit is on scripting data and control structures, so the programs are identified here.
ls is the directory listing program, akin to “dir” in Windows. -l is the option that causes the relevant attributes to be listed on a single line.
shasum computes a SHA-1 cryptographic checksum of the file given to it as an argument. This is a string that depends upon the contents of the file. If you change the file, the probability that the checksum will not change is (roughly) 2-128. So it’s not perfect, but it’s pretty good, and it beats keeping another copy of the file around!
diff takes two files and prints out the lines in each that are not in the other. We’ll explain more about the output of this one later on.

## Slide 8: Steps 3, 4, and 5
Let’s do this incrementally.
  This way we can check each substep as we go along.
  This greatly simplifies testing!
Notes: As you know, a basic rule of programming is that you don’t write a whole program and then test it. Do it incrementally. The exercises for this section are framed that way, as are the parts of each exercise. We test each step as we complete it.

## Slide 9: Steps 3 and 4
We do these incrementally:
Substep 1. List the attributes of the files.
Substep 2. Save them in a “master file.”
Substep 3. Do Substep 1 again, comparing the results to what is saved in the master file; print the lines that changed.
Substep 4. Format the output nicely, to list only the files.
Substep 5. Add options to allow the generation, deletion of the “master file.”
Notes: Step 3 (“Figure out your approach”) and Step 4 (“Implement it”) are combined here because after each incremental change, you want to test that (a) the change worked, and (b) the change didn’t mess up anything that already existed. So we’ll follow this basic scheme but add lots of error-checking and robustness along the way.

## Slide 10: Substep 1
List the attributes of the files.
ls –l file_name lists the first seven attributes:
$ ls -l myls.sh
-rw-rw-r-- 1 bishop bishop 20 Jan 15 14:42 myls.sh
shasum file_name gives the hash: $ shasum myls.sh
d5d3697e2f0d48b42e48763e45fecb9092f843ac myls.sh
We need to combine these onto a single line
  That will allow us to use diff, which compares lines ...
Notes: Now we start with the scripting.
Recall we will be comparing two files, both of which contain attributes. One file will be the “master list” of the values those attributes and the checksum should have. The second contains the values they have now. To make using diff easy, we want to put the attributes and checksum on one line. Hence the need to combine them.
This also acts as a lesson in how to interpolate command output into other commands … read on!
myls.sh is in the directory 13.SeS_Unit2_AdvancedControl_DataFiles in Secure Scripting Module . Note the shasum may produce something different if the end of line markers are changed from newline to something else.

## Slide 11: Files: Creating, Reading, and Writing to Files
Python offers file handlers by using the function open()
Syntax:
fileObject = open(“filename”, “mode”)
Where:
fileObject is the variable to add the file object.
Mode:
  ‘r’– read mode, used when the file is only being read.
  ‘w’– write mode, used to edit new information to an existing file.
  ‘a’– appending mode, used to add new data to the end of the file.
  ‘r+’– special read and write mode, used to handle both actions when working with a file

## Slide 12: Processing Files Attributes
Processing files considering file attributes in Python is possible
File system provides a list of attributes to:
  Read
  Write
  Execute
Depending on the
  Owner
  Group
  Other users
The library os in Python provides functions that allow to check for these attributes

## Slide 13: More Tests
These functions belong to the library os.
-os.path.exists(‘name’) True if name is the name of a file that exists.
-os.access(‘name’,mode) True if name is the name of a file that the user is allowed to execute the mode stated.
-Mode os.R_OK − Value to include the mode to test the readability of path.
os.W_OK – Value to include the mode to test the writability of path.
os.X_OK -- Value to include in the mode to determine if path can be executed.
Notes: This just emphasizes that you can test lots of things. Some of these will pop up in Unit 3 (Advanced Scripting) of the module; we will discuss them then.
Again, you should put quotes around str and name when you use them, in case they contain blanks.

## Slide 14: Looping
Looping helps us to process independent items (strings, values, files) in a list of items by using repetitive-structures
Python provides different repetitive structures such as
  for-loop, and
  while-loop
  else-loop
Elements: loops work along
  the iterable keyword in, that allows us to process one-by-one each item in a list, and
The function range(), that provides a list of items allowing to have a starting and ending point to process data
Notes: If someone asks why you can’t just do “ls –l *”, it’s because you then have to figure out how to put the shasum for each file afterward. You can do this with join (1), but I wanted to show control structures like loops.
Also, the technique we will use will miss files whose names begin with a “.”. That’s a good exercise for people who are familiar with Linux, but I wanted to avoid it.

## Slide 15: The for Loop
for i in list:
  actions
This executes actions for each item in list.
In actions, i refers to the current list element.
Notes: The notion of list can be introduced from Secure Scripting. 11.SeS_Unit2_AdvancedControl_Presentation (slide 14).

## Slide 16: Example: for1.py
cservin$ python for1.py
1
2
3
4
5
1. for i in range(1,6):
2. print (i)
Execution and Output:
Notes: Introduce the build-in command range. The range function returns a Python list object. It is a easy way to generate a list of integers.

## Slide 17: Loop Control Commands
continue
  Skip the remainder of the loop and begin the next iteration.
break
  Immediately leave the (innermost) loop.
for-else
  The else clause executes when the loop completes normally, meaning that the loop was not interrupted by any break.
Notes: These are just like the C, C++, and Java.
The for-else helps to keep track interruption within the loop execution. Useful when to validate data that doesn't satisfy user’s constraints

## Slide 18: Example: for2.py
cservin$ python for2.py
1
3
5
1. for i in range(1,6):
2. if i%2 == 0:
3. continue
4. print (i)
Execution and Output:
Notes: for2.py
We take advantage of the constructs from Python to perform arithmetic operations such as modulo/reminder.
The function range will provide the consecutive values from 1 to 6 (non-inclusive 6).
For each of the value I
Checks if is divisible by 2 (i.e., if the value is even). If it happens to be true after the evaluation, we will use the reserved word continue, allowing to skip the current iteration.
If i % 2 == 0
continue
In case the condition is true, we can simply print the current value of i.

## Slide 19: First Problem
List the words in the file dict.txt that contain “gry”.
Understand the problem.
  A file contains words.
  What is a word? That depends on the data in the file.
  Some words may have the character sequence “gry” in them.
  List them.
  Print them, one per line, on the standard output.
Notes: This problem corresponds to Lab Exercise 1 in 05.SeSPython_Unit1_TheBasics_Lab.
Here, we state the problem and start breaking it down along the lines discussed earlier.
First, what is a word? One common definition is any nonempty sequence of alphabetic characters. But does that include numbers, apostrophes, and hyphens? That depends on interpretation. So let’s look at the data and see if it suggests anything.

## Slide 20: First Problem (Cont.)
Understand the format of the data.
  The file “dict.txt” has 1 word per line.
  Therefore we can reframe the problem as: List the lines in the file dict.txt that contain the sequence of letters “gry”.
Notes: This slide corresponds to Lab Exercise 1, Part A, in 05.SeSPython_Unit1_TheBasics_Lab.
Looking at the file, it’s clear the file is a list of words, one per line, so we just say that a word is whatever is on a single line.
This highlights the need to understand the data to be analyzed. Here, text files generally have multiple words per line. On those files, you would need to use a completely different tactic. But with one word per line, the problem is much easier to solve.

## Slide 21: Find the Right Command
Figure out your approach.
  See if there is a built-in command that looks for character sequences in a file.
    We will be using a for loop
    The command in will help to iterate through each word per line
    Use conditional statement to check if target is in word
  On Linux environment, we are trying to simulate what grep does, which is one of the most commonly used for this on scripting.
Notes:   This slide corresponds to Lab Exercise 1, Part B, in 05.SeSPython_Unit1_TheBasics_Lab.
  Note that you can use a pattern to express a character sequence. Here it’s easy as there are no metacharacters to be matched.
A useful tool for finding commands is the command apropos (1):
  Try apropos match.
  Look down the output for something that says “print lines matching” or something similar and has a “(1)” on it; the (1) means it’s a user command.

## Slide 22: Process File Content
1. myFile = open(“dict.txt”, ‘r’)
2. for word in myFile:
3. print(word)
>cservin$ python3 processFileContent.py
….
zygomorphous
zymogene
Zyrenian
ZZ
Notice that after each line, there is a space (‘\n’)
You can get rid of the new line by using the .strip() function on each word
word.strip()
Execution and Output:
Notes: The information on this slides references the files located in 10.SeSPython_Unit2_AdvancedControl_DataFiles

## Slide 23: Checking for Occurrence
For every word we process, we must compare if it matches with the target that we are looking for
Use the conditional statement inside the loop, so for every word that is processed, it checks for a true value
1. myFile = open(“dict.txt”, ‘r’)
2. for word in myFile:
3. if(‘gry’ in word):
4. print(word.strip())
cservin$ python3 checkForOccurrence.py
agrypnia
agrypnode
arthrogryposis
grylle
grypanian
gryph
...
Execution and Output:
Notes: The information on this slides references the files located in 10.SeSPython_Unit2_AdvancedControl_DataFiles

## Slide 24: Lab Exercise 1
This exercise allows you to try out some of the things you have seen.
  If your script worked, you should get the result described in Part C of Lab Exercise 1. This is Step 5, “Test it.”
Completing this exercise will help you:
  Understand how to write a very basic script.
  Practice reading a description of programs that the script can call upon.
Notes: This is Lab Exercise 1, Part C, in 05.SeSPython_Unit1_TheBasics_Lab.
Step 5 of the approached outlined on Slides 11-12, “Test it,” is included in Part C of Lab Exercise 1. We’re doing only basic testing. Part C of Lab Exercise 1 says what the script should print. Here are the words:
agrypnia
agrypnode
arthrogryposis
grylle
grypanian
gryph
gryposis
pouggry

## Slide 25: User Interaction
Now let’s allow the user to specify the sequence.
python3 lookfor1.py abcde
will look for lines that contain the sequence “abcde”.
Notes: From this point on, we will use the script written for Exercise 1 as the basis for developing the other scripts.
Also, throughout we will use “sh” to run the scripts, rather than making the scripts executable. You can change this if you like; just remember to have the students make the scripts executable so they will run. Slide 5 shows how to do this. The information on this slides references the files located in 10.SeSPython_Unit2_AdvancedControl_DataFiles

## Slide 26: Still Not Safe
1. import sys
2. myFile = open(“dict.txt”, ‘r’)
3. for word in myFile:
4. if(sys.argv[1] in word):
5. print(word.strip())
Call this script mycat.py.
File x contains “This is file x”.
File y contains “This is file y”.
File x y contains “This is file x y”.
  Note the name of this last file is x followed by a blank followed by y.
Notes: The quotation marks are interpreted by the shell – but you type the script name and arguments in a shell! So the command interpreter that you’re using interprets the quotation marks. And so the first argument is the string x followed by blank followed by y (“x y”). When replacing $1, though, there are no quotation marks – so cat sees this as two arguments, x and y.
The next two slides show this in detail.
The script mycat is in the directory 07.SeS_Unit1_TheBasics_DataFiles in the Secure Scripting Module.

## Slide 27: Here We Go …
Why do neither of these display “This is file x y”?
>cservin$ python mycat.py x
This is file x
>cservin$ python mycat.py y
This is file y
>cservin$ python mycat.py x y
This is file x
Notes: This shows the error. The files are in 07.SeS_Unit1_TheBasics_DataFiles in the Secure Scripting Module, so you can actually demonstrate this, or have the students try it out.

## Slide 28: Look at the Script
sys.argv[1] is “x y” so the string “x y” replaces argv[1] in the script.
So the command in it is
cat x y
— which is not what we want.
Instead, make that second line
cat “argv[1]”
Notes: The solution is to put the argument variable reference in the script in quotes. You must use double quotes here; if you use single quotes, then the $1 will be interpreted as the string “$1”, not as “x y”. Slide 27 asks the students this question, so if you didn’t mention the difference between double quotes and single quotes, you might want to do so now.
To re-emphasize this: $ is a metacharacter, so single quotes strip it of its “meta” power.

## Slide 29: Got It!
mycat “x y”
Now, argv[1] is “x y”, so after replacement, the command in the second line is
cat “x y”
as the " " keeps the original form of the argument.
And we see …
cservin$ python mycat.py "x y"
This is file x y

## Slide 30: Another Example: forFilesProcessing.py
The following routine prints the files that are in the current working directory (.)
Need to import the library os to obtain access to the file system
import os
for root, dirs, files in os.walk("."):
for filename in files:
print("file name: ",filename)
Notes: Script that allows to combine concepts from fundamentals in scripting such as processing directories and files. This time we use the power of loops and the directives of Python to process individually the directories and files.
The concept of nested-loops is introduced in this slide,
Since for every item found in the current directory ( . ) we hold the
Root
Directories
Files
Python allows to keep three control variables while processing the content of the current directory.
In the nested loop
for filename in files:
Now we consider each file that is been hold by the variable files.
Notice that this variable files correspond to the list containing the current directory.
The only task we do in this example is to print the files.
In similar fashion, if your interest is to print ONLY the directories, then modify the inner loop as follows:
for dirName in dirs:
print ”Directory name: ",dirName

## Slide 31: A Gotcha!
import os
for root, dirs, files in os.walk("."):
for dirName in dirs:
print(dirName)
In similar fashion, if the user is interested in only access or printing the directories, the code shall look as follows
The function walk, returns a tuple, which are lists of items. In this example, os.walk(“.”) provides a 3 lists: root, dirs, and files
Notes: The following implementation provides a process to identify directories and files. The concept that may be lost is the tokenization process by using the " ". The library os provides a rich libraries to deal with files and directories.

## Slide 32: The subprocess library
Allows Python to call a command from the OS and execute its output
import subprocess
proc = subprocess.Popen([“command"],
stdout = subprocess.PIPE,
shell=True)
The variable proc now contains the results of execution the command through the subprocess.
The function communicate() permits to execute the commands and will provide a tuple:
  result: containing the result by executing the provided command, and
  Err: a potential error that may occur while executing the command
(result, err) = proc.communicate()

## Slide 33: Script Construct
Example:
cservin$ python combining.py
at Sun Jan 21 20:29:25 MST 2018 i was cservin
import subprocess
proc = subprocess.Popen(["date"], stdout = subprocess.PIPE, shell=True)
(date, err) = proc.communicate()
proc = subprocess.Popen(["whoami"], stdout = subprocess.PIPE, shell=True)
(who, err) = proc.communicate()
print("at ",date.rstrip()," i was ",who.rstrip())
Notes: This construct is very widely used. Just to be clear, it’s the back single quote; on most keyboards, it’s the key next to the 1, and the shift is the tilde (~).
date is a command to print the date: Sun Jul 10 09:18:21 PDT 2016
whoami prints the name of the logged-in user: bishop
Note the interpolation. Again, remind people that the “$ “ is a prompt, not something you type.

## Slide 34: Combining …
So put them together …
import subprocess
proc = subprocess.Popen(["ls -l combining.py"],
stdout = subprocess.PIPE, shell=True)
(ls, err) = proc.communicate()
proc = subprocess.Popen(["shasum combining.py"],
stdout = subprocess.PIPE, shell=True)
(sha, err) = proc.communicate()
print (ls.rstrip()," ",sha.rstrip())
cservin$ python combining.py
-rwxr-xr-x@ 1 cservin staff 301 Jan 21 20:35 combining.py 8d07eac225d247b30bcb97637f071b849cb76fe5 combining.py
Notes: Now we see how to do the combination. As explained in Unit 1, echo is a command that just prints its arguments. In this case, that’s the output of the two commands. The trailing newlines on both are removed.
Notice that the filename “myls.sh” is repeated in the output. In this context, we don’t care, because it will be repeated in both the master file and the new file we generate each time for checking. But if you want to remove it, use awk. The command would be
awk '{print $1, $2, $3, $4, $5, $6, $7, $8, $10, $11}’
Explaining that in awk, $1 refers to the first field might confuse beginners. On the other hand, it does show the importance of single quotes (‘) because they prevent $1 from being interpreted by the shell; if you have time and the desire, you can use this to reinforce the function of single quotes. Double quotes (“) would cause the $1 to be interpreted by the shell.

## Slide 35: Too much code… Hard to code
Challenge:
Despite the fact that Python is powerful to call system functions, the routines to invoke the functions may be long, confusing and cryptic
Also, if we don’t know how to use them may produce a security leak
Solution
Defining functions can assist to internally call specific system functions without providing the long routine
Helps to reuse code for future functions call, and
Simplify your code

## Slide 36: Functions
Functions allows us to use the divide and conquer technique in scripting, allowing robust coding to be more
  Debuggable/testable
  Modularized
  Clean
Python functions: function definition and function call.
Function definition Syntax:
def functionName():
commands
commands
Function call Syntax:
  functionName()
Notes: Functions are useful for encapsulating commonly-used commands.

## Slide 37: Function Definition
def incrementby1(i):
return i + 1
This function takes one argument and adds 1 to it.
To call it, say incrementby1(num),
Where num can be an argument from the program.
Example: functionExample1.py
1. import sys
2. def main():
3. print (incrementby1(int(sys.argv[1])))
4. def incrementby1(i):
5. return i+1
6. main()
cservin$ python functionExample1.py 5
6
Notes: Here, the function prints a value. The caller will capture it using the ` … ` .
The data file "fn1“ is in the directory 19.SeS_Unit3_AdvancedScripting_DataFiles in the Secure Scripting Module.

## Slide 38: Another Way: Reference to Global Variables
def incrementby1():
  global result
  result = result+1
}
Invoke a function that performs operations with a global variable.
Use the global keyword to reference to a global context.
Example: functionExample2.py
1. result = 0
2. def main():
3. incrementby1()
4. print (result)
5. def incrementby1():
6. global result
7. result = result + 1
8. main()
cservin$ python functionExample2.py
1
Notes: A second way to return a value is to assign it to a variable. By default, all variables in the Bourne shell scripts are global, so RESULT is available outside the function.
This method has the advantage of allowing a function to output multiple values—just have multiple variables!
The data file "fn2“ is in the directory 19.SeS_Unit3_AdvancedScripting_DataFiles in the Secure Scripting Module.

## Slide 39: Here’s a More Complicated One
Script to round to the nearest 10: functionExample3.py
1. import sys
2. def main():
3. print (roundto10(13))
4. print (roundto10(50))
5. print (roundto10(97))
6.
7. def roundto10(num):
8. units = num%10
9. tens = num/10
10. if units >= 5:
11. tens = tens+1
12. return tens*10
13. main()
Output:
cservin$ python functionExample3.py
10
50
100
Notes: This function rounds its integer to the nearest 10s and prints the result. Note the escaped * in the last expr to prevent the interpreter from expanding it.
Again, reference RETVAL to get the computed value.
The data file “round“ is in the directory 19.SeS_Unit3_AdvancedScripting_DataFiles in the Secure Scripting Module.

## Slide 40: Divide and Conquer Technique
1. import subprocess
2. def call(args):
3. proc = subprocess.Popen([args], stdout = subprocess.PIPE,
4. shell=True)
5. (out, err) = proc.communicate()
6. return out
7.
8. def main():
9. cmd = input(">")
callAndPrint(cmd)
11.
12. def callAndPrint(args):
13. args = call(args)
14. for result in args:
15. print (result+"\n")main()

## Slide 41: Explanation
Line 2 – 6: Define the function “call”. which basically encapsulates the functionality discussed on Slide 32.
Line 8—10: Define the function “main”, which basically triggers the program and shows notion to computer user to interact with program.
Line 12—15: Define the helper function “callAndPrint” that will display the content of a given set of results.

## Slide 42: Lab Exercise 1 (Unit 2 Lab)
In this exercise you try out the looping and inline execution with ` presented here.
After doing this exercise, you will:
  Understand the way looping works in scripts
  Understand how the script interacts with the file system
  Gain practice at writing a more complex script
Notes: The exercise on this slide correlates to Lab Exercise 1 located in 11.SeSPython_Unit2_AdvancedControl_Lab.docx

## Slide 43: The Master File
We need to record the file attributes in a “master file”.
We will use a variable to store the location of this file.
  That way, we can change the location easily.
This also contributes to robustness.
  Just change the variable value; you do not need to change anything else in the script.
Notes: In practice, this master file would be written to a secure area, preferably on write-once media so it could not be erased, even by accident. To update it, you would use a different name or replace the media.
The master file will contain a list of attributes and checksums generated in the same way that we scan the file system for checking.

## Slide 44: Example Use
import os
X="MasterList"
if( os.path.isfile(X) ):
print ("File ",X," exists“)
else:
print ("File ",X," does not exist“)
Notes: This is a straightforward test for existence. The name of the file being tested is “MasterList”.

## Slide 45: Exiting Cleanly
To terminate the python a script, call the exit command with a status code:
import sys
  sys.exit(0)
    All went well, and the script worked; the user can relax.
  sys.exit(1)
    Something went wrong, and the script terminated.
    You can use any non-zero number instead of 1; convention is to have the specific number (“exit status code”) indicate the error that caused termination.
Notes: This is a standard Linux/*nix convention: exit code 0 means success, anything else means failure.
Note this is exactly the opposite of most programming languages’ conventions, where 0 means false and non-zero means true.
The if and other conditional statements are aware of this backwardness, and assume it. You might reiterate that [ is a command; if the conditions given to it are true, it exits with status code 0, and if not, it exits with status code 1. So on Slide 27, if “-e “$X”” is true, [ exits with status code 0, and the body of the if is executed. If not, “-e “$X”” is false, and so [ exits with status code 1, and the body of the else is executed.

## Slide 46: Multiple Conditions
To test if file name is a regular file and is not the file named “gleep”, do this:
import os
import sys
FILE = input("Name of File: ")
if( FILE != "gleep" and not os.path.isfile(FILE)):
print ("not gleep, and a regular file”)
sys.exit(0)
The usage of parentheses help to identify multiple conditions
Notes: These are the Boolean operators. The file “bool1.py” has the above if statement (FILE receives input from the user to specify the name). The file “bool2.py” has an example of using parentheses. The files “bool1.py” and “bool2.py” are located in 09.SeSPython_Unit2_AdvancedControl_DemoScripts

## Slide 47: With Parentheses
1. print (“we assign 100 to X and test if 0 <= SX <= 10 or SX is 100”)
2. X=100
3. if (X >= 0) and (X <= 100 or X <=10):
3. print (“X, which is ”,X,”, is between 0 and 10 or is 100”)
4. else:
5. print (“X, which is ”,X,”, is not between 0 and 10 or is 100”)
6. sys.exit (0)
cservin$ python bool2.py
we assign 100 to X and test if 0 <= $X <= 10 or $X is 100
X, which is 100 , is between 0 and 10 or is 100
Execution and Output:
Notes: These are the Boolean operators. The file “bool2.py” has more examples, including the above. The file “bool2.py” is located in 09.SeSPython_Unit2_AdvancedControl_DemoScripts

## Slide 48: Lab Exercise 2
This exercise introduces you to working with variables and using their values to control execution.
After completing this exercise, you will be able to:
  Define and use variables in a script
  Combine conditions using a Boolean
  Exit a script without going to the end of the script file
Notes: The exercise on this slide correlates to Lab Exercise 2 located in 11.SeSPython_Unit2_AdvancedControl_Lab.docx

## Slide 49: Temporary Files
Like regular files, but:
  Deleted after use
  Usually named by something unique to the process
  Libraries:
    import os
    import tempfile
Notes: These are used to hold transient data. They are traditionally placed in the /tmp or /usr/tmp directories. Here, they would be placed in a protected area, but for expository purposes we will use the traditional place.
$$ is a value that corresponds to the PID of the shell process that is executing this script. It’s a 4- to 6-digit number (usually).

## Slide 50: Temporary Files (cont)
1. import os
2. import tempfile
3. print (‘Creating a temporary file:’)
4. processID = str(os.getpid()) #get process id from sys
5. filename = “/tmp/”+processID+”.txt” #create a file name with pid
6. tmp = open(filename, ‘w’) #open as write file current tmp file
7. print (‘tmp file:’, tmp) #print info of the current tmp file
8. tmp.close() #close the file before leave
9. os.remove(filename) #clean up the tmp file explicitly
Creates the temporary file named by the process id number
cservin$ python testTemp.py
Creating a temporary file:
tmp file: <open file '/tmp/10464.txt', mode 'w' at 0x10790d660>
Execution and Output:
Notes: These are used to hold transient data. They are traditionally placed in the /tmp or /usr/tmp directories. Here, they would be placed in a protected area, but for expository purposes we will use the traditional place.
$$ is a value that corresponds to the PID of the shell process that is executing this script. It’s a 4- to 6-digit number (usually).

## Slide 51: Comparing Two Files in Shell
diff file1 file2
Example:
  $ diff x1 x2
  1,2c1,2
  < Tue Jun 12 14:26:18 PDT 2016
  < bishop
  ---
  > Tue Jun 24 14:27:23 PDT 2016
  > Bishop
Notes: The files x1 and x2 are in the directory 13.SeS_Unit2_AdvancedControl_DataFiles located in the Secure Scripting Module. Note each has a third line, but they are the same so diff does not report them.

## Slide 52: Comparing Two Files in Python
Option #1
  Invoke diff by using library os
Option #2
  Use the filecmp library along with other Python functions and loops
  1. import filecmp
  2. print (filecmp.cmp(‘x1’, ‘x1’))
  3. print (filecmp.cmp(‘x1’, ‘x2’))
cservin$ python3 mydiff.py
True
False
Execution and Output:

## Slide 53: Lab Exercise 3
This exercise allows you to adapt what you wrote to use a temporary file, and see how to compare files.
After completing this exercise, you will be able to:
  Adapt a script to carry out a task that differs slightly from the original script
  Create, use, and delete a temporary file
Notes: The exercise on this slide correlates to Lab Exercise 3 located in 11.SeSPython_Unit2_AdvancedControl_Lab.docx

## Slide 54: Putting File Names In Order
sorted()
  Output a sorted list of input lines
set()
  Given an input of items, find duplicate items and print only the first one
Notes: sort takes its input as a sequence of lines, sorts them (here in the underlying character set ordering, usually ASCII), and prints the sorted lines.
uniq looks for matching lines in its input. When it finds a sequence of lines that match, only the first is printed. Otherwise, the line is printed.

## Slide 55: Lab Exercise 4
This exercise requires you to combine two scripts into a single script.
After completing this exercise, you will be able to:
  Merge two scripts into a single working script
  Work with multiple variables in a script
  Change the output of a script to be more readable
Notes: The exercise on this slide correlates to Lab Exercise 4 located in 11.SeSPython_Unit2_AdvancedControl_Lab.docx

## Slide 56: Command-Line Options
These change the way a script works, but only for that particular execution. For example:
scan.py –d will delete the MasterList
scan.py –g will generate the MasterList
scan.py
  Without any options, scan.sh compares the current file attributes with those stored in MasterList and prints the names of the files that have changed attributes or content.
Notes: Options are a common way to control the behavior of a program or script, so they should be considered an integral part of the scripting.
These are just examples. Sometimes an option will have an argument. For example, you might have an option –mfilename to rename the master file to filename.

## Slide 57: Processing an Option
Define variable associated with option
Set variable as dictated by option
  Define DELMASTER as yes if –d given, no if not
  Define GENMASTER as yes if –g given, no if not
Notes: This translates the arguments into variable values. Then you can test the values as opposed to looking for the options repeatedly.
Here, the variable names reflect what their values signify. By default, you do not generate a master file, nor do you delete it.
Here’s a good place to look for a robustness problem: what does using the options together mean? It could be that you first delete the master file and then generate a new one. We will choose to allow only one option, though, so we need to check for both being given.

## Slide 58: Example: -d, -g
  1. import sys
  2. DELMASTER = False
  3. GENMASTER = False
  4. print (len(sys.argv))
  5. for i in range(1, len(sys.argv)):
  6. if sys.argv[i] == “-d”:
  7. DELMASTER = True
  8. elif sys.argv[i] == “-g”:
  9. GENMASTER = True
  10. else:
  11. print (sys.argv[i], “is not a valid option”)
  12. sys.exit(1)
Notes: The case statement is like a switch statement. If there are multiple matching cases, only the first is done. Note the “;;” at the end of the line; that means the case ends.
The cases are really patterns. In them:
“*” matches 0 or more characters
“?” matches exactly 1 character
[abc] matches any character between the brackets. If the first is ^, then it matches any character not between the brackets.
Corner cases: To include a”]”, make it the first character. To include a “^”, make it any character other than the first.

## Slide 59: Lab Exercise 5
This exercise gives you practice in using command line options to control the actions of a script
After completing this exercise, you will be able to:
  Use if statements to choose an action based on the value of a variable
  Perform sanity checking on the options and on the combination of options
Notes: The exercise on this slide correlates to Lab Exercise 5 located in 11.SeSPython_Unit2_AdvancedControl_Lab.docx

## Slide 60: To Wrap Up
To solve a problem using a script:
  Understand the problem.
  Understand the format of the data.
  Figure out your approach.
  Implement it.
  Test it.
We did this with script to find files that changed in a directory.
Defining functions that helps the testing process.
This approach keeps you focused on the goal and how to achieve it.